Specification of Subject of Performance – Part B VZ

Program name: 	Arbostat evaluation software

Use of the device:

The software for TreeQinetic instruments. Windload analysis for trees analogous to Eurocode EN 1991-1-4-1 / DIN 1055-4 for the dynamic gust reaction of tree crowns. Evaluation of static load test data (measurements of force vs. fibre strain and root plate tilt) to be used in expertises on tree risk assessment by trained consulting arborists incl. tables of guideline values for wind structure (National Annexes to Eurocode 1 for Britain, France, Germany and the Netherlands) and green wood properties as well as references for parameters used in the dynamic and static analysis.

The licence's validity is not limited in time and may be used in one company's office at up to 3 workstations.

The price includes technically required updates for the duration of 2 years.

Training for the Pull Test Method

The training consists of 4 units, which are held on 4 days in sequence. Participation on all days is mandatory for acquiring the licence for using Arbostat software.

Unit 1: Introduction - Tree biomechanics and basics of pull tests with the following contents:

- engineering concepts and safety

- fracture, Hook's Law, elastic limit

- tipping behaviour of trees

- wind effects on urban sites

- dynamics of wind and trees

- pull test demonstration

Unit 2: Hands-on training in pull tests (TreeQinetic system) with the following contents:

- measuring technology, devices

- pull test and sensor setup

- data acquisition and validation

- limits in the pull test, risks

Unit 3: Evaluation with Arbostat software with the following contents:

- wind structure, tree response

- beam theory, material properties

- tipping load, soil and roots

- practical application in Arbostat

Unit 4: Practical exercises. In this unit, all acquired knowledge will be applied.

- practical pull tests

- evaluations with Arbostat

The delivered software shall then be installed by the participant at one workstation in the contracting authority’s premises. The licence shall be granted for unlimited time.

The subject of delivery shall include information on the installation method.

Technical requirements for the subject of performance:

- 	Operation in WINDOWS environment

- 	Full functionality after the end of paid user support period

- 	It can be a fully integrated system of several separate products or modules.